## Slide 1
Chapter 2
Digital Design and Computer Architecture: ARM® Edition
Sarah L. Harris and David Money Harris

## Slide 2
Introduction
Boolean Equations
Boolean Algebra
From Logic to Gates
Multilevel Combinational Logic
X’s and Z’s, Oh My
Karnaugh Maps
Combinational Building Blocks
Timing
Chapter 2 :: Topics

## Slide 3
A logic circuit is composed of:
Inputs
Outputs
Functional specification
Timing specification
Introduction

## Slide 4
Nodes
  Inputs: A, B, C
  Outputs: Y, Z
  Internal: n1
Circuit elements
  E1, E2, E3
  Each a circuit
Circuits

## Slide 5
Combinational Logic
  Memoryless
  Outputs determined by current values of inputs
Sequential Logic
  Has memory
  Outputs determined by previous and current values of inputs
Types of Logic Circuits

## Slide 6
Every element is combinational
Every node is either an input or connects to exactly one output
The circuit contains no cyclic paths
Example:
Rules of Combinational Composition

## Slide 7
Functional specification of outputs in terms of inputs
Example: S = F(A, B, Cin)
Cout = F(A, B, Cin)
Boolean Equations

## Slide 8
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Minterm: product that includes all input variables
ABC, ABC, ABC
Maxterm: sum that includes all input variables
(A+B+C), (A+B+C), (A+B+C)
Some Definitions

## Slide 9
Y = F(A, B) =
Sum-of-Products (SOP) Form
All equations can be written in SOP form
Each row has a minterm

## Slide 10
Y = F(A, B) =
Sum-of-Products (SOP) Form
All Boolean equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)

## Slide 11: Sum-of-Products Form
Y = F(A, B) = AB + AB
All Boolean equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)
Sum-of-Products (SOP) Form

## Slide 12: Sum-of-Products Form
Y = F(A, B) = AB + AB = Σ(1, 3)
All Boolean equations can be written in SOP form
Each row has a minterm
A minterm is a product (AND) of literals
Each minterm is TRUE for that row (and only that row)
Form function by ORing minterms where output is 1
Thus, a sum (OR) of products (AND terms)
Sum-of-Products (SOP) Form

## Slide 13
All Boolean equations can be written in POS form
Each row has a maxterm
Product-of-Sums (POS) Form

## Slide 14
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Product-of-Sums (POS) Form

## Slide 15
Y = F(A, B) = (A + B)●(A + B)
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Form function by ANDing maxterms where output is 0
Thus, a product (AND) of sums (OR terms)
Product-of-Sums (POS) Form

## Slide 16
Y = F(A, B) = (A + B)●(A + B) = Π(0, 2)
All Boolean equations can be written in POS form
Each row has a maxterm
A maxterm is a sum (OR) of literals
Each maxterm is FALSE for that row (and only that row)
Form function by ANDing maxterms where output is 0
Thus, a product (AND) of sums (OR terms)
Product-of-Sums (POS) Form

## Slide 17
Boolean Equations Example
You are going to the cafeteria for lunch
  You won’t eat lunch (E=0)
  If it’s not open (O=0) or
  If they only serve corndogs (C=1)
Write a truth table for determining if you will eat lunch (E).

## Slide 18
You are going to the cafeteria for lunch
  You won’t eat lunch (E=0)
  If it’s not open (O=0) or
  If they only serve corndogs (C=1)
Write a truth table for determining if you will eat lunch (E).
Boolean Equations Example

## Slide 19: SOP & POS Form
SOP – sum-of-products
POS – product-of-sums

## Slide 20
E = (O + C)(O + C)(O + C)
= Π(0, 1, 3)
E = OC
= Σ(2)
SOP & POS Form
SOP – sum-of-products
POS – product-of-sums

## Slide 21
Axioms and theorems to simplify Boolean equations
Like regular algebra, but simpler: variables have only two values (1 or 0)
Duality in axioms and theorems:
  ANDs and ORs, 0’s and 1’s interchanged
Boolean Algebra

## Slide 22
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR

## Slide 23
Boolean Axioms
Number | Axiom | Name
A1 | B = 0 if B ≠ 1 | Binary Field
A2 | 0 = 1 | NOT
A3 | 0 • 0 = 0 | AND/OR
A4 | 1 • 1 = 1 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | AND/OR
Dual: Replace: • with +
0 with 1

## Slide 24
Boolean Axioms
Number | Axiom | Dual | Name
A1 | B = 0 if B ≠ 1 | B = 1 if B ≠ 0 | Binary Field
A2 | 0 = 1 | 1 = 0 | NOT
A3 | 0 • 0 = 0 | 1 + 1 = 1 | AND/OR
A4 | 1 • 1 = 1 | 0 + 0 = 0 | AND/OR
A5 | 0 • 1 = 1 • 0 = 0 | 1 + 0 = 0 + 1 = 1 | AND/OR
Dual: Replace: • with +
0 with 1

## Slide 25
Boolean Theorems of One Variable
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements

## Slide 26
Boolean Theorems of One Variable
Number | Theorem | Name
T1 | B • 1 = B | Identity
T2 | B • 0 = 0 | Null Element
T3 | B • B = B | Idempotency
T4 | B = B | Involution
T5 | B • B = 0 | Complements
Dual: Replace: • with +
0 with 1

## Slide 27
Boolean Theorems of One Variable
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identity
T2 | B • 0 = 0 | B + 1 = 1 | Null Element
T3 | B • B = B | B + B = B | Idempotency
T4 | B = B |  | Involution
T5 | B • B = 0 | B + B = 1 | Complements
Dual: Replace: • with +
0 with 1

## Slide 28
B 1 = B
B + 0 = B
T1: Identity Theorem

## Slide 29
B 1 = B
B + 0 = B
T1: Identity Theorem

## Slide 30
B 0 = 0
B + 1 = 1
T2: Null Element Theorem

## Slide 31
B 0 = 0
B + 1 = 1
T2: Null Element Theorem

## Slide 32
B B = B
B + B = B
T3: Idempotency Theorem

## Slide 33
B B = B
B + B = B
T3: Idempotency Theorem

## Slide 34
B = B
T4: Identity Theorem

## Slide 35
B = B
T4: Identity Theorem

## Slide 36
B B = 0
B + B = 1
T5: Complement Theorem

## Slide 37
B B = 0
B + B = 1
T5: Complement Theorem

## Slide 38
Recap: Basic Boolean Theorems
Number | Theorem | Dual | Name
T1 | B • 1 = B | B + 0 = B | Identity
T2 | B • 0 = 0 | B + 1 = 1 | Null Element
T3 | B • B = B | B + B = B | Idempotency
T4 | B = B |  | Involution
T5 | B • B = 0 | B + B = 1 | Complements
Dual: Replace: • with +
0 with 1

## Slide 39
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
T7 | (B•C) • D = B • (C • D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | Distributivity
T9 | B• (B+C) = B | Covering
T10 | (B•C) + (B•C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus

## Slide 40
How do we prove these are true?
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
T7 | (B•C) • D = B • (C • D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | Distributivity
T9 | B• (B+C) = B | Covering
T10 | (B•C) + (B•C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus

## Slide 41
How to Prove
Method 1: Perfect induction
Method 2: Use other theorems and axioms to simplify the equation
  Make one side of the equation look like the other

## Slide 42
Proof by Perfect Induction
Also called: proof by exhaustion
Check every possible input value
If the two expressions produce the same value for every possible input combination, the expressions are equal

## Slide 43
Example: Proof by Perfect Induction
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
0 0
0 1
1 0
1 1
B C BC CB

## Slide 44
0 0
0 0
0 0
1 1
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
Example: Proof by Perfect Induction
0 0
0 1
1 0
1 1
B C BC CB

## Slide 45
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
T7 | (B•C) • D = B • (C • D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | Distributivity
T9 | B• (B+C) = B | Covering
T10 | (B•C) + (B•C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus

## Slide 46
T7: Associativity
Number | Theorem | Name
T7 | (B•C) • D = B • (C • D) | Associativity

## Slide 47
T8: Distributivity
Number | Theorem | Name
T8 | B • (C + D) = (B•C) + (B•D) | Distributivity

## Slide 48
T9: Covering
Number | Theorem | Name
T9 | B• (B+C) = B | Covering

## Slide 49
T9: Covering
Prove true by:
Method 1: Perfect induction
Method 2: Using other theorems and axioms
Number | Theorem | Name
T9 | B• (B+C) = B | Covering

## Slide 50
T9: Covering
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)
Method 1: Perfect Induction
Number | Theorem | Name
T9 | B• (B+C) = B | Covering

## Slide 51
T9: Covering
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)

## Slide 52
T9: Covering
Method 1: Perfect Induction
0 0
1 0
1 1
1 1
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
0 0
0 1
1 0
1 1
B C (B+C) B(B+C)

## Slide 53
T9: Covering
Number | Theorem | Name
T9 | B• (B+C) = B | Covering
Method 2: Prove true using other axioms and theorems.

## Slide 54
T9: Covering
Method 2: Prove true using other axioms and theorems.
B•(B+C) = B•B + B•C T8: Distributivity
= B + B•C T3: Idempotency
= B•(1 + C) T8: Distributivity
= B•(1) T2: Null element
= B T1: Identity
Number | Theorem | Name
T9 | B• (B+C) = B | Covering

## Slide 55
T10: Combining
Prove true using other axioms and theorems:
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | Combining

## Slide 56
T10: Combining
Prove true using other axioms and theorems:
B•C + B•C = B•(C+C) T8: Distributivity
= B•(1) T5’: Complements
  = B T1: Identity
Number | Theorem | Name
T10 | (B•C) + (B•C) = B | Combining

## Slide 57
T11: Consensus
Number | Theorem | Name
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus
Prove true using (1) perfect induction or (2) other axioms and theorems.

## Slide 58
Boolean Theorems of Several Vars
Number | Theorem | Name
T6 | B•C = C•B | Commutativity
T7 | (B•C) • D = B • (C • D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | Distributivity
T9 | B• (B+C) = B | Covering
T10 | (B•C) + (B•C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus

## Slide 59
Dual: Replace: • with +
0 with 1
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
Boolean Theorems of Several Vars

## Slide 60
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
Boolean Theorems of Several Vars
Warning: T8’ differs from traditional algebra:
OR (+) distributes over AND (•)

## Slide 61
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
Boolean Theorems of Several Vars
Axioms and theorems are useful for simplifying equations.

## Slide 62
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals

## Slide 63
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals
  Recall:
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C

## Slide 64
Simplifying an Equation
Reducing an equation to the fewest number of implicants, where each implicant has the fewest literals
  Recall:
  Implicant: product of literals
  ABC, AC, BC
  Literal: variable or its complement
A, A, B, B, C, C
Simplifying the equation is also called minimizing the equation

## Slide 65
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P

## Slide 66
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A

## Slide 67
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A

## Slide 68
Proving the “Simplification” Theorem
“Simplification” theorem
PA + A = P + A
Method 1: PA + A = PA + (A + AP) T9’ Covering
= PA + PA + A T6 Commutativity
= P(A + A) + A T8 Distributivity
= P(1) + A T5’ Complements
= P + A T1 Identity

## Slide 69
“Simplification” theorem
PA + A = P + A
Method 2: PA + A = (A + A) (A + P) T8’ Distributivity
= 1(A + P) T5’ Complements
= A + P T1 Identity
Proving the “Simplification” Theorem

## Slide 70
T11: Consensus
Number | Theorem | Name
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus
Prove using other theorems and axioms:

## Slide 71
T11: Consensus
Number | Theorem | Name
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | Consensus
Prove using other theorems and axioms:
B•C + B•D + C•D
= BC + BD + (CDB+CDB) T10: Combining
= BC + BD + BCD+BCD T6: Commutativity
= BC + BCD + BD + BCD T6: Commutativity
= (BC + BCD) + (BD + BCD) T7: Associativity
= BC + BD T9’: Covering

## Slide 72
# | Theorem | Dual | Name
T6 | B•C = C•B | B+C = C+B | Commutativity
T7 | (B•C) • D = B • (C•D) | (B + C) + D = B + (C + D) | Associativity
T8 | B • (C + D) = (B•C) + (B•D) | B + (C•D) = (B+C) (B+D) | Distributivity
T9 | B • (B+C) = B | B + (B•C) = B | Covering
T10 | (B•C) + (B•C) = B | (B+C) • (B+C) = B | Combining
T11 | (B•C) + (B•D) + (C•D) = (B•C) + (B•D) | (B+C) • (B+D) • (C+D) = (B+C) • (B+D) | Consensus
Boolean Theorems of Several Vars

## Slide 73
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A

## Slide 74
Y = AB + AB
Simplifying Boolean Equations
Example 1:

## Slide 75
Y = AB + AB
Y = A T10: Combining
or
= A(B + B) T8: Distributivity
= A(1) T5’: Complements
= A T1: Identity
Simplifying Boolean Equations
Example 1:

## Slide 76
Simplification methods
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A

## Slide 77
Y = A(AB + ABC)
Example 2:
Simplifying Boolean Equations

## Slide 78
Y = A(AB + ABC)
= A(AB(1 + C)) T8: Distributivity
= A(AB(1)) T2’: Null Element
= A(AB) T1: Identity
= (AA)B T7: Associativity
= AB T3: Idempotency
Example 2:
Simplifying Boolean Equations

## Slide 79
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A
Simplification methods

## Slide 80
Y = A’BC + A’ Recall: A’ = A
Example 3:
Simplifying Boolean Equations

## Slide 81
Y = A’BC + A’ Recall: A’ = A
Note:
A‘ is shorthand for A.
But use the tick symbol (‘) only when typing.
It’s easy to lose ticks (‘) when writing by hand!
It is strongly recommended that you simplify equations by writing by hand.
Example 3:
Simplifying Boolean Equations

## Slide 82
Y = A’BC + A’ Recall: A’ = A
= A’ T9’ Covering: X + XY = X
or
= A’(BC + 1) T8: Distributivity
= A’(1) T2’: Null Element
= A’ T1: Identity
Example 3:
Simplifying Boolean Equations

## Slide 83
Y = AB’C + ABC + A’BC
Example 4:
Simplifying Boolean Equations

## Slide 84
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A
Simplification methods

## Slide 85
Y = AB’C + ABC + A’BC
= AB’C + ABC + ABC + A’BC T3’: Idempotency
= (AB’C+ABC) + (ABC+A’BC) T7’: Associativity
= AC + BC T10: Combining
Example 4:
Simplifying Boolean Equations

## Slide 86
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A
Simplification methods

## Slide 87
Y = AB + BC +B’D’ + AC’D’
Method 1:
Y = AB + BC + B’D’ + (ABC’D’ + AB’C’D’) T10: Combining
= (AB + ABC’D’) + BC + (B’D’ + AB’C’D’) T6: Commutativity
T7: Associativity
= AB + BC + B’D’ T9: Covering
Method 2:
Y = AB + BC + B’D’ + AC’D’ + AD’ T11: Consensus
= AB + BC + B’D’ + AD’ T9: Covering
= AB + BC + B’D’ T11: Consensus
Example 5:
Simplifying Boolean Equations

## Slide 88
Distributivity (T8, T8’) B (C+D) = BC + BD
  B + CD = (B+ C)(B+D)
Covering (T9’) A + AP = A
Combining (T10) PA + PA = P
Expansion P = PA + PA
A = A + AP
Duplication A = A + A
“Simplification” theorem PA + A = P + A
    PA + A = P + A
Simplification methods

## Slide 89
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Example 6:
Simplifying Boolean Equations

## Slide 90
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = BC, Z = DE and rewrite equation
Y = (A+X)(A+Z) substitution (X=BC, Z=DE)
= A + XZ T8’: Distributivity
= A + BCDE substitution
or
Y = AA + ADE + ABC + BCDE T8: Distributivity
= A + ADE + ABC + BCDE T3: Idempotency
= A + ADE + ABC + BCDE
= A + ABC + BCDE T9’: Covering
= A + BCDE T9’: Covering
Example 6:
Simplifying Boolean Equations

## Slide 91
Y = (A + BC)(A + DE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = BC, Z = DE and rewrite equation
Y = (A+X)(A+Z) substitution (X=BC, Z=DE)
= A + XZ T8’: Distributivity
= A + BCDE substitution
or
Y = AA + ADE + ABC + BCDE T8: Distributivity
= A + ADE + ABC + BCDE T3: Idempotency
= A + ADE + ABC + BCDE
= A + ABC + BCDE T9’: Covering
= A + BCDE T9’: Covering
Example 6:
Simplifying Boolean Equations
This is called
multiplying out
an expression to get
sum-of-products (SOP) form.

## Slide 92
SOP – sum-of-products
POS – product-of-sums
E = (O + C)(O + C)(O + C)
= Π(0, 1, 3)
E = OC
= Σ(2)
Review: Canonical SOP & POS Forms

## Slide 93
An expression is in sum-of-products (SOP) form when all products contain literals only.
SOP form: Y = AB + BC’ + DE
NOT SOP form: Y = DF + E(A’+B)
SOP form: Z = A + BC + DE’F
Multiplying Out: SOP Form

## Slide 94
Y = (A + C + D + E)(A + B)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = (C+D+E), Z = B and rewrite equation
Y = (A+X)(A+Z) substitution (X=(C+D+E), Z=B)
= A + XZ T8’: Distributivity
= A + (C+D+E)B substitution
= A + BC + BD + BE T8: Distributivity
or
Y = AA+AB+AC+BC+AD+BD+AE+BE T8: Distributivity
= A+AB+AC+AD+AE+BC+BD+BE T3: Idempotency
= A + BC + BD + BE T9’: Covering
Example:
Multiplying Out: SOP Form

## Slide 95
An expression is in product-of-sums (POS) form when all sums contain literals only.
POS form: Y = (A+B)(C+D)(E’+F)
NOT POS form: Y = (D+E)(F’+GH)
POS form: Z = A(B+C)(D+E’)
Factoring: POS Form

## Slide 96
Y = (A + B’CDE)
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: X = B’C, Z = DE and rewrite equation
Y = (A+XZ) substitution (X=B’C, Z=DE)
= (A+B’C)(A+DE) T8’: Distributivity
= (A+B’)(A+C)(A+D)(A+E) T8’: Distributivity
Example 1:
Factoring: POS Form

## Slide 97
Y = AB + C’DE + F
Apply T8’ first when possible: W+XZ = (W+X)(W+Z)
Make: W = AB, X = C’, Z = DE and rewrite equation
Y = (W+XZ) + F substitution W = AB, X = C’, Z = DE
= (W+X)(W+Z) + F T8’: Distributivity
= (AB+C’)(AB+DE)+F substitution
= (A+C’)(B+C’)(AB+D)(AB+E)+F T8’: Distributivity
= (A+C’)(B+C’)(A+D)(B+D)(A+E)(B+E)+F T8’: Distributivity
= (A+C’+F)(B+C’+F)(A+D+F)(B+D+F)(A+E+F)(B+E+F) T8’: Distributivity
Example 2:
Factoring: POS Form

## Slide 98
DeMorgan’s Theorem
Number | Theorem | Name
T12 | B0•B1•B2… = B0+B1+B2… | DeMorgan’s Theorem

## Slide 99
DeMorgan’s Theorem
The complement of the product
is the
sum of the complements
Number | Theorem | Name
T12 | B0•B1•B2… = B0+B1+B2… | DeMorgan’s Theorem

## Slide 100
DeMorgan’s Theorem: Dual
# | Theorem | Dual | Name
T12 | B0•B1•B2… = B0+B1+B2… | B0+B1+B2… = B0•B1•B2… | DeMorgan’s Theorem

## Slide 101
DeMorgan’s Theorem: Dual
The complement of the product
is the
sum of the complements.
# | Theorem | Dual | Name
T12 | B0•B1•B2… = B0+B1+B2… | B0+B1+B2… = B0•B1•B2… | DeMorgan’s Theorem

## Slide 102
DeMorgan’s Theorem: Dual
The complement of the product
is the
sum of the complements.
Dual: The complement of the sum
is the
product of the complements.
# | Theorem | Dual | Name
T12 | B0•B1•B2… = B0+B1+B2… | B0+B1+B2… = B0•B1•B2… | DeMorgan’s Theorem

## Slide 103
Y = AB = A + B
Y = A + B = A B
DeMorgan’s Theorem

## Slide 104
Y = (A+BD)C
DeMorgan’s Theorem Example 1

## Slide 105
Y = (A+BD)C
= (A+BD) + C
= (A•(BD)) + C
= (A•(BD)) + C
= ABD + C
DeMorgan’s Theorem Example 1

## Slide 106
Y = (ACE+D) + B
DeMorgan’s Theorem Example 2

## Slide 107
Y = (ACE+D) + B
= (ACE+D) • B
= (ACE•D) • B
= ((AC+E)•D) • B
= ((AC+E)•D) • B
= (ACD + DE) • B
= ABCD + BDE
DeMorgan’s Theorem Example 2

## Slide 108
Y = AB = A + B
Y = A + B = A B
DeMorgan’s Theorem

## Slide 109
Backward:
  Body changes
  Adds bubbles to inputs
Forward:
  Body changes
  Adds bubble to output
Bubble Pushing

## Slide 110
Bubble Pushing
What is the Boolean expression for this circuit?

## Slide 111
What is the Boolean expression for this circuit?
Y = AB + CD
Bubble Pushing

## Slide 112
Begin at output, then work toward inputs
Push bubbles on final output back
Draw gates in a form so bubbles cancel
Bubble Pushing Rules

## Slide 113
Bubble Pushing Example

## Slide 114
Bubble Pushing Example

## Slide 115
Bubble Pushing Example

## Slide 116
Bubble Pushing Example

## Slide 117
Two-level logic: ANDs followed by ORs
Example: Y = ABC + ABC + ABC
From Logic to Gates

## Slide 118
Inputs on the left (or top)
Outputs on right (or bottom)
Gates flow from left to right
Straight wires are best
Circuit Schematics Rules

## Slide 119
Wires always connect at a T junction
A dot where wires cross indicates a connection between the wires
Wires crossing without a dot make no connection
Circuit Schematic Rules (cont.)

## Slide 120
Multiple-Output Circuits
Example: Priority Circuit
Output asserted
corresponding to most
significant TRUE input

## Slide 121
Example: Priority Circuit
Output asserted
corresponding to most
significant TRUE input
Multiple-Output Circuits

## Slide 122
Priority Circuit Hardware

## Slide 123
Don’t Cares

## Slide 124
Contention: circuit tries to drive output to 1 and 0
  Actual value somewhere in between
  Could be 0, 1, or in forbidden zone
  Might change with voltage, temperature, time, noise
  Often causes excessive power dissipation
Warnings:
  Contention usually indicates a bug.
  X is used for “don’t care” and contention - look at the context to tell them apart.
Contention: X

## Slide 125
Floating, high impedance, open, high Z
Floating output might be 0, 1, or somewhere in between
  A voltmeter won’t indicate whether a node is floating
Tristate Buffer
Floating: Z

## Slide 126
Floating nodes are used in tristate busses
  Many different drivers
  Exactly one is active at once
Tristate Busses

## Slide 127
Boolean expressions can be minimized by combining terms
K-maps minimize equations graphically
PA + PA = P
Karnaugh Maps (K-Maps)

## Slide 128
Circle 1’s in adjacent squares
In Boolean expression, include only literals whose true and complement form are not in the circle
Y = AB
K-Map

## Slide 129
3-Input K-Map

## Slide 130
3-Input K-Map
Y = AB + BC

## Slide 131
Complement: variable with a bar over it
A, B, C
Literal: variable or its complement
A, A, B, B, C, C
Implicant: product of literals
ABC, AC, BC
Prime implicant: implicant corresponding to the largest circle in a K-map
K-Map Definitions

## Slide 132
Every 1 must be circled at least once
Each circle must span a power of 2 (i.e. 1, 2, 4) squares in each direction
Each circle must be as large as possible
A circle may wrap around the edges
Circle a “don't care” (X) only if it helps minimize the equation
K-Map Rules

## Slide 133
4-Input K-Map

## Slide 134
4-Input K-Map

## Slide 135
4-Input K-Map

## Slide 136
K-Maps with Don’t Cares

## Slide 137
K-Maps with Don’t Cares

## Slide 138
K-Maps with Don’t Cares

## Slide 139
Multiplexers
Decoders
Combinational Building Blocks

## Slide 140
Selects between one of N inputs to connect to output
log2N-bit select input – control input
Example: 2:1 Mux
Multiplexer (Mux)

## Slide 141
Logic gates
  Sum-of-products form
Tristates
  For an N-input mux, use N tristates
  Turn on exactly one to select the appropriate input
Multiplexer Implementations

## Slide 142
Using mux as a lookup table
Logic using Multiplexers

## Slide 143
Reducing the size of the mux
Logic using Multiplexers

## Slide 144
N inputs, 2N outputs
One-hot outputs: only one output HIGH at once
Decoders

## Slide 145
Decoder Implementation

## Slide 146
OR the minterms
Logic Using Decoders

## Slide 147
Delay: time between input change and output changing
How to build fast circuits?
Timing

## Slide 148
Propagation delay: tpd = max delay from input to output
Contamination delay: tcd = min delay from input to output
Propagation & Contamination Delay

## Slide 149
Delay is caused by
  Capacitance and resistance in a circuit
  Speed of light limitation
Reasons why tpd and tcd may be different:
  Different rising and falling delays
  Multiple inputs and outputs, some of which are faster than others
  Circuits slow down when hot and speed up when cold
Propagation & Contamination Delay

## Slide 150
Critical (Long) Path: tpd = 2tpd_AND + tpd_OR
Short Path: tcd = tcd_AND
Critical (Long) & Short Paths

## Slide 151
When a single input change causes an output to change multiple times
Glitches

## Slide 152
What happens when A = 0, C = 1, B falls?
Glitch Example

## Slide 153
Glitch Example (cont.)

## Slide 154
Fixing the Glitch

## Slide 155
Because of synchronous design conventions (see Chapter 3), glitches don’t cause problems.
It’s important to recognize a glitch: in simulations or on oscilloscope.
We can’t get rid of all glitches – simultaneous transitions on multiple inputs can also cause glitches.
Why Understand Glitches?